## Slide 1: GEOM20013: WEEK 5 TUTORIAL

## Slide 2: Assignment 3
Assignment 3 Overview
Victorian Rail Authority (VRA) are proposing new high-speed rail.
They have 4 proposed alignments, you have to decided the most appropriate one based on your analysis.
There is not necessarily one correct answer, how you conduct your analysis, your justifications and quality of report are what will be marked.
Are provided with the alignments and DEM datasets
Analysis required:
    new rail cannot be built on a slope steeper than 25 degrees
    track cannot follow a path prone to flooding

## Slide 3: A3: Proposed Alignments

## Slide 4: Additional Analysis
Additional Data Examples
Waterways
Vegetation
Townships
Existing infrastructure
Additional Analysis Options
Flooding, water crossings
Protected vegetation, vegetation clearing
Potential major stops, potential for new major townships along route, property acquisitions
Crossing of existing infrastructure, re-engineering of existing infrastructure

## Slide 5: Sourcing additional data
Additional data examples
  Rivers: https://www.data.vic.gov.au/data/dataset/modified-rivers
  Rainfall: http://www.bom.gov.au/climate/how/newproducts/IDCmrgrids.shtml
    Data is in an ASCII format. Use the ASCII to Raster tool to convert to a raster and visualise for analysis
  Roads: https://vicroadsopendata-vicroadsmaps.opendata.arcgis.com/datasets/vicroads-declared-roads
  Additional data sources:
    Geoscience Australia: http://www.ga.gov.au/
    Vic Government: https://www.data.vic.gov.au/
    AURIN: https://aurin.org.au/
Further resources can be found under the ‘Additional Information and Resources’ tab in the LMS

## Slide 6: Tools Demonstration
Clip
  Alters the size of the raster to the extents of another feature and helps with reducing the processing time in further raster analysis

## Slide 7: Tools Demonstration
Aspect
  Determines the direction of the slope
Slope
  Calculates the change in elevation from neighbouring cells

## Slide 8: Tools Demonstration
Reclassify
  Changes the values in a raster to suit the required analysis
Raster Calculator
  Executes Map Algebra expressions and outputs a raster

## Slide 9: Further Information
Further tools and information can be found in workflow the LMS:
Assessment -> A3 Decision Making in GIS -> Workflow